## Slide 1: Quantitative Analysis of BGP Route Leaks
Benjamin Wijchers Benno Overeinder

## Slide 2: The Problem With Route Leaks
Route leaks are not route hijacks (in my definition)
  route hijack: originate prefixes you do not “own”
  route leaks: forward BGP announcements you shouldn’t according policies
Route leaks not easy to detect
Potential security risk
  examples Belarusian and Iceland traffic misdirection

## Slide 3: Business Relations and Route Leaks
ASes have business relationship
  Client pays provider
  Provider provides transit
  Peers share client routes
Routing should reflect business relations
  But in practice not always the case
    Route leak

## Slide 4: The Valley Free Rule
Relations between ASes:
  Customer-provider
  Peer-peer
  Siblings
Valley Free Rule:
  C2P(*) – P2P (1|0) – P2C (*)

## Slide 5: The Valley Free Rule

## Slide 6: Origins of Route Leaks
Misconfiguration
Malicious
  Man in the middle
Intentional
  Indirect peering
    IXP
    Research / Educational
  Complex relations
Find characteristics for categorizing

## Slide 7: Why Analyse Them?
Counter-measures planned
  part of ongoing IETF SIDR WG activities
  discussions in the context of BGPSEC
Traffic routes incorrectly causing:
  ASes paying for transit of other ASes clients
  Potentially slower connections
  Potential hijacking of data (mitm)
Not much statistics available

## Slide 8: Previous Work
Jared Mauch
  Detection without relation data
  Not much statistics
    List of route leaks
    General counts

## Slide 9: Detecting Valleys
Relations between ASes
  Non-disclosure agreement
  Inferred relations
BGP data dumps to investigate
  RIPE Remote Route Collector
  RouteViews
ASPATH attribute
  Shows path of ASes traversed

## Slide 10: Relation Inferences
Lixin Gao
  Valley free rule
Ricardo Oliveira et al (UCLA)
  Every non-tier-1 AS is (indirect) client (or peer) of tier-1
Matthew Lucky et al (CAIDA)
    C2P to reach global connectivity
    Peering clique at top of topology
    No cycles of C2P links
CAIDA chosen for project
  Validation of relations
  No valley freeness used in inference

## Slide 11: Methodology
CAIDA relationship data
  Combined with siblings data
BGP MRT files from
  RIPE RIS RRC00
  Routeviews WIDE
  Routeviews Oregon
Custom BGPdump
Detecting valleys

## Slide 12: Methodology (2)
All valleys in database with
  violation type
    e.g. P2C-C2P
  AS Leak triplet
    leaked from, leaker and receiver
  duration
    check updates for same AS & prefix

## Slide 13: About the results
Current results from 1 month from RIPE, Oregon and WIDE
  ~4% of routes investigated valley
  Over 36 000 000 valley announces detected

## Slide 14: Distribution of Violation Types
Top left area are no real valleys
P2P-P2P occurs most frequently
Notes: 17,6 % siblings

## Slide 15: Distribution of Durations
Peaks at <2 seconds and 17-32 seconds
  Default MRAI Cisco: 30 seconds
  Probably unintentional

## Slide 16: Most Frequent Leak Triplets
Duration > 1 minute
~12% of valleys found in top 10
Next challenge
  categorize in classes

## Slide 17: Geography of Most Frequent Leaks

## Slide 18: Top Leaks Further Investigated
WIDE appears to provide transit for peer APNIC
APAN, WIDE and APNIC are all research ASes
  who commonly have “special” relationships
Likely intentional behaviour

## Slide 19: Top Leaks Further Investigated
Both AS12880 and AS48159 from Iran
  possible merge -> sibling
  cannot say for certain with data available
WHOIS AS12880 no mention of AS48159
  WHOIS AS48159 mentions AS12880 as default route

## Slide 20: Top Leaks Further Investigated
Different policies IPv4 and IPv6
  mp-import: afi ipv6.unicast from AS6939 action pref=150; accept ANY
  mp-import: afi ipv4.unicast from AS6939 action pref=150; accept AS-HURRICANE

## Slide 21: Conclusion
Most route leaks are peer routes propagated to other peers
~65% valleys are very short-lived (< minute)
  but ~6% very persistent (> day)
About 12% AS triplets reoccur frequently in found route leaks
  most of them “special” relations
  not enough knowledge to define others

## Slide 22: Future Work
Broader date range
  monthly reports, history with less storage
Separate relation data IPv4/IPv6
RPSL data usage for automatic detection of complex relations

## Slide 23: Questions
Acknowledgments
  Jared Mauch
  Stella Vouteva